## Slide 2
A force represents the action of one body on another and is generally characterized by its point of application , its magnitude , and its direction. Forces acting on a given particle, however, have the same point of application. Each force considered in this chapter will thus be completely defined by its magnitude and direction.
Vectors are defined as mathematical expressions possessing magnitude and direction, which add according to the parallelogram law.
ADDITION OF VECTORS
The diagonal that passes through A represents the sum of the vectors P and Q , and this sum is denoted by P + Q

## Slide 3
From the parallelogram law, we can derive an alternative method for determining the sum of two vectors. This method, known as the triangle rule ,
The sum of the two vectors can thus be found by arranging P and Q in tip-to-tail fashion and then connecting the tail of P with the tip of Q .s
sum of the three vectors could have been obtained directly, as shown in Fig., by arranging the given vectors in tip to- tail fashion and connecting the tail of the first vector with the tip of the last one. This is shown as the polygon rule for the addition of vectors.

## Slide 4: Resolution of a Force into components
The process of splitting up the given force in to a number of components, without changing its effect on body is called resolution of a force.

## Slide 5
Resolution along any two directions ( Not mutually perpendicular)
O
F
α
β
Y’
x’
α + β ≠ 90º

## Slide 6
O
F
180 – α - β
α
β
Y’
x’
α
Fy
Fx
Fy

## Slide 7
=
=

## Slide 8
Resolution into Rectangular components (mutually perpendicular)
  Most common 2D resolution of a force vector
  Express in terms of unit vectors ,

## Slide 9
q
x
y

## Slide 10
Scalar components – can be positive and negative

## Slide 11
1) A force of 800 N is exerted on a bolt A as shown in Figure. Determine the horizontal and vertical components of the force

## Slide 14
Rectangular components are convenient for finding the sum or resultant of two (or more) forces which are concurrent
RECTANGULAR COMPONENTS OF A FORCE.
Two vectors of unit magnitude, directed respectively along the positive x and y axes, will be introduced at this point. These vectors
are called unit vectors and are denoted by i and j , respectively

## Slide 16
P
S
Q
R = P + S + Q
A

## Slide 17
P
S
Q
R = P + S + Q
A
Py j
Px i
Sy j
Sx i
Qx i
Qy j

## Slide 19
A
Ry j
Rx i
Rx = Px + Sx + Qx Ry = Py + Sy + Qy
Rx = ∑Fx Ry = ∑Fy

## Slide 20
1. Determine the magnitude and direction of the resultant of five forces. Specify its direction measured counter clockwise from the positive x axis.
F1 = 40 kN
F3 = 60 kN
F2 = 50 kN
F5 = 55 kN
F4 = 45 kN
50
50
70
60

## Slide 21
F1 = 40 kN
F3 = 60 kN
F5 = 55 kN
F4 = 45 kN
50
50
70
60
F2 = 50 kN

## Slide 22
F1 = 40 kN
50
Fy = 40 sin50
Fx = 40 cos 50

## Slide 23
F2 = 50 kN
Fx = 50 cos 90
Fx = 50 sin 90

## Slide 24
F3 = 60 kN
70
F3 = 60 cos 70
F3 = 60 sin 70

## Slide 25
Sr. No. | Force | x- component | y- component
1 | F1 = 40 kN | 40 cos50◦ | 40 sin50◦
2 | F2 = 50 kN | 50 cos90◦ | 50 sin90◦
3 | F3 = 60 kN | - 60 sin70◦ | 60 cos70◦
4 | F4 = 45 kN | -45 cos60◦ | - 45 sin60◦
5 | F5 = 55 kN | 55 cos50◦ | - 55 sin50◦
 |  | Rx = -17.32 | Ry = 20.06

## Slide 26
Sr. No. | Force | x- component | y- component
1 | F1 = 40 kN | + 25.71 | + 30.64
2 | F2 = 50 kN | 0 | + 50.00
3 | F3 = 60 kN | - 56.38 | + 20.52
4 | F4 = 45 kN | -22.50 | - 38.97
5 | F5 = 55 kN | +35.35 | - 42.13
 |  | Rx = -17.32 | Ry = 20.06

## Slide 27
R = Rx i + Ry j
R = (-17.32 kN) i + (20.06 kN) j

## Slide 28
R = (-17.32 kN) i + (20.06 kN) j

## Slide 29
F1 = 40 kN
F3 = 60 kN
F2 = 50 kN
F5 = 55 kN
F4 = 45 kN
50
50
70
60

## Slide 30
2. Four forces acts on bolt A as shown. Determine the resultant forces on the bolt.
R = 199.6 N

## Slide 33
3.

## Slide 34
The problems considered in the first part of this chapter involved only two dimensions; they could be formulated and solved in a single plane. In this section and in the remaining sections of the chapter, we will discuss problems involving the three dimensions of space.
Consider a force F acting at the origin O of the system of rectangular coordinates x, y, z. To define the direction of F , we draw the vertical plane OBAC containing F
This plane passes through the vertical y axis; its orientation is defined by the angle f it forms with the xy plane. The direction of F within the plane is defined by the angle u y that F forms with the y axis. The force F may be resolved into a vertical component F y and a horizontal component F h ;
The corresponding scalar components are

## Slide 35
But F h may be resolved into two rectangular components F x and F z along the x and z axes, respectively. This operation, shown in Fig c , is carried out in the xz plane. We obtain the following expressions for the corresponding scalar components:

## Slide 36
Clearly, the vector λ is a vector whose magnitude is equal to 1 and whose direction is the same as that of F

## Slide 37
The vector λ is referred to as the unit vector along the line of action of F

## Slide 38
In many applications, the direction of a force F is defined by the coordinates of two points, M ( x 1 , y 1 , z 1 ) and
N ( x 2 , y 2 , z 2 ), located on its line of action
Consider the vector MN joining M and N
and of the same sense as F . Denoting its scalar components by d x , d y ,d z , respectively, we write

## Slide 39
from which it follows that the scalar components of F are, respectively

## Slide 40
Problem 4

## Slide 42
Problem 5

## Slide 44
Problem. 6

## Slide 45
Solution:-

## Slide 49
A
B
D
C
(-450,600,0)
(500,600,360)
(0,600,-320)
(0,0,0)
W

## Slide 58
(0,5.6,0)
(-4.2,0,0)
(2.4,0,4.2)
(0,0,-3.3)

## Slide 63
Take away of the chapter

## Slide 64
A force F in three-dimensional space can be resolved into rectangular components F x , F y , and F z
Forces in space

## Slide 67
Knowing that the tension in AC is TAC = 20 kN, determine the required values of tension TAB and TAD so that the resultant of the three forces applied at A is vertical and calculate resultant.
TAB = 37.09 kN
TAD = 61.12 kN
R = - 110.05 kN
Unsolved 1

## Slide 68
Unsolved 2

## Slide 69
Unsolved 3

## Slide 70
Unsolved 4

## Slide 71
The resultant of the three concurrent space forces at A is R = (-788 j)N. Find the magnitude of F1, F2 and F3 forces.
F1 = 154 N
F2 = 320 N
F3= 400 N
Unsolved 5